## Slide 1: 8051 Microcontroller and its application
-By Rishabh Maurya A06
Kshitij Kadam A08

## Slide 2: Introduction to Microcontrollers
A microcontroller (MCU for microcontroller unit) is a small computer on a single metal-oxide-semiconductor (MOS) integrated circuit (IC) chip.
A microcontroller contains one or more CPUs (processor cores) along with memory and programmable input/output peripherals.
Types of Microcontrollers
  ARM core processors (many vendors)
  ARM Cortex-M cores are specifically targeted toward microcontroller applications
  Freescale 68HC11 (8-bit), and others based on the Motorola 6800 family
  Intel 8051, also manufactured by NXP Semiconductors, Infineon and many other

## Slide 3: Intel 8051
In 1981, Intel introduced an 8-bit microcontroller called the 8051. It was referred as system on a chip because it had 128 bytes of RAM, 4K byte of on-chip ROM, two timers, one serial port, and 4 ports (8-bit wide), all on a single chip.
When it became widely popular, Intel allowed other manufacturers to make and market different variations of 8051 with its code compatible with 8051.
Comparison between 8051 Family Members
Feature | 8051 | 8052 | 8031
ROM(bytes) | 4K | 8K | 0K
RAM(bytes) | 128 | 256 | 128
Timers | 2 | 3 | 2
I/O pins | 32 | 32 | 32
Serial port | 1 | 1 | 1
Interrupt sources | 6 | 8 | 6

## Slide 4: Features of 8051 Microcontroller
4KB bytes on-chip program memory (ROM)
128 bytes on-chip data memory (RAM)
Four register banks
128 user defined software flags
8-bit bidirectional data bus
16-bit unidirectional address bus
32 general purpose registers each of 8-bit
16 bit Timers (usually 2, but may have more or less)
Three internal and two external Interrupts
Four 8-bit ports,(short model have two 8-bit ports)
16-bit program counter and data pointer
8051 may also have a number of special features such as UARTs, ADC, Op-amp, etc.

## Slide 5: Applications of 8051
Automatic washing machine motor control system.
Bidirectional Visitor Counter
DC Motor Controller Using AT89C51
Digital alarm clock
Line Follower Robot using 8051
Digital clap counter
Street Lights that Glow on Detecting Vehicle Movement?
A Smart Anti-theft System for Vehicle Security

## Slide 6: Street Lights that Glow on Detecting Vehicle Movement
Generally, street lights are switched on for whole night and during the day, they are switched off. But during the night time, street lights are not necessary if there is no traffic. Saving of this energy is very important factor these days as energy resources are getting reduced day by day.?
Alternatives for natural resources are very less and our next generations may face lot of problems because of lack of these natural resources?
This application is easily achievable using 8051, let us see the circuit diagram to understand the working.?

## Slide 7: Circuit Diagram

## Slide 8: Components
Microcontroller Section
    AT89C52 Microcontroller
    AT89C52 Programmer Board
    11.0592 MHz Quartz Crystal
    22pF Ceramic Capacitor
    2 x 10K Resistor
    10uF Electrolytic Capacitor
    Push Button
IR Transmitter and Receiver Section
    8 x IR LED (IR Transmitters)
    8 x 470R Resistor
    8 x Photo Diode (IR Receivers)
    8 x 3.3K Resistor
    1K x 8 Resistor Pack
Load Section
    8 x 2N2222 NPN Transistors
    8 x 100R Resistor
    8 x White LEDs

## Slide 9: Principle of Operation
The principle behind the working of the project lies in the functioning of IR Sensor. We are going to use a Transmissive type IR Sensor in this project.
In Transmissive IR Sensor, the IR transmitter and receiver are placed facing each other so that IR receiver always detects IR Rays emitted by the IR Transmitter.
If there is an obstacle between the IR Transmitter and Receiver, the IR Rays are blocked by the obstacle and the IR Receiver stops detecting the IR Rays.
This can be configured to turn ON or OFF the LEDs (or street lights) with the help of microcontroller.

## Slide 10: Working
The IR transmitter is placed directly in line of sight with IR receiver, so that the IR receiver continuously receives infrared rays. Once the IR receiver receives infrared rays, the microcontroller will detect Logic 1. If the infrared rays are blocked by some means, the microcontroller will detect logic 0.
So, the program for the microcontroller must be written in such a way that it will turn ON the LEDs, which means here the street lamp, when it detects Logic 0 and it will turn OFF the LEDs, when it detects Logic 1.
Consider the two IR sensors i.e. IR Transmitter and IR Receiver are placed on the either side of the road. As per the circuit diagram, the IR receivers are connected to the PORT0 and the LEDs are connected to the PORT2 of the microcontroller.
At the beginning, when there is no obstacle, the IR receiver continuously detects IR light transmitted by the IR Transmitter. When a car or any other vehicle blocks any of the IR sensor, the microcontroller will turn ON the immediate three LEDs.
If the car blocks the first IR sensor, the first three LEDs are turned ON by the microcontroller. As the car moves forward and blocks the second IR sensor, the corresponding next three LEDs will be turned ON and the first LED of the previous set is turned OFF. The process continues this way for all the IR Sensors and LEDs.

## Slide 11: Program
LED_NL1 BIT P2.7 LED_NL2 BIT P2.4 LED_NL3 BIT P2.1 LED_RD1S1 BIT P2.0 LED_RD2S1 BIT P2.2 LED_RD1S2 BIT P2.3 LED_RD2S2 BIT P2.5 LED_RD1S3 BIT P2.6 LED_RD2S3 BIT P3.0 IP_LDR BIT P1.0 IP_IR1 BIT P1.1 IP_IR2 BIT P1.2 IP_IR3 BIT P1.3 CONT1 EQU 25H CONT2 EQU 26H CONT3 EQU 27H CONT4 EQU 28H
ORG 0000H LJMP MAIN ORG 0003H RETI ORG 000BH RETI ORG 0013H RETI ORG 001BH LJMP TIMER_1 RETI ORG 0023H RETI TIMER_1: CLR TR1 MOV TL1,#0B2H MOV TH1,#03AH
MOV A,CONT1 INC A CJNE A,#20D,TIMER_NXT3 MOV A,CONT2 JZ TIMER_NXT1 MOV CONT2,A
CJNE A,#0D,TIMER_NXT1
TIMER_NXT1: MOV A,CONT3 JZ TIMER_NXT2 MOV CONT3,A CJNE A,#0D,TIMER_NXT2 SETB LED_RD1S2 SETB LED_RD2S2 TIMER_NXT2: MOV A,CONT4 JZ TIMER_NXT3
MOV CONT4,A CJNE A,#0D,TIMER_NXT3
SETB LED_RD1S3 SETB LED_RD2S3 TIMER_NXT3: SETB TR1
RETI MAIN: MOV PSW,#00H MOV SP,#70H MOV P0,#0FFH
MOV P1,#0FFH MOV P2,#0FFH MOV P3,#0FFH MOV TMOD,#10H MOV TCON,#00H
MOV SCON,#00H MOV TL1,#0B2H MOV TH1,#03AH MOV IE,#88H MOV IP,#00H SETB LED_NL1 SETB LED_NL2 SETB LED_NL3 SETB LED_RD1S1 SETB LED_RD2S1 SETB LED_RD1S2 SETB LED_RD2S2 SETB LED_RD1S3 SETB LED_RD2S3 MOV CONT1,#00H MOV CONT2,#00H MOV CONT3,#00H MOV CONT4,#00H
SETB TR1 MAIN_LP: JNB IP_LDR,NXT4
CLR LED_NL1 CLR LED_NL2 CLR LED_NL3 NXT1: JB IP_IR1,NXT2 CLR LED_RD1S1 CLR LED_RD2S1 MOV CONT2,#05H NXT2: JB IP_IR2,NXT3 CLR LED_RD1S2 CLR LED_RD2S2 MOV CONT3,#05H NXT3: JB IP_IR3,NXT4 CLR LED_RD1S3 CLR LED_RD2S3 MOV CONT4,#02H NXT4: JNB IP_LDR,NXT5
SETB LED_NL1 SETB LED_NL2 SETB LED_NL3 SETB LED_RD1S1 SETB LED_RD2S1 SETB LED_RD1S2 SETB LED_RD2S2 SETB LED_RD1S3 SETB LED_RD2S3 NXT5: LJMP MAIN_LP END

## Slide 12: Advantages
If the lighting system implements all LED lights, the cost of the maintenance can be reduced as the life span and durability of LEDs is higher than Neon based lights which are normally used as street lights.
As the lights are automatically turned ON or OFF, huge amount of energy can be saved.
Conclusion
Click to add text

## Slide 13: Thank you